## Slide 1
SFWMD final meeting
June16, 2015
H. Carl Fitz
EcoLandMod, Inc.
Wading Bird Habitat Suitability:
Everglades Landscape Model Applications
Some of the FCE &
related models

## Slide 2: Project Goals
Evaluate ecological responses to changes in WCA-2A regulation schedule
  How will soils respond?
  How will vegetation respond?
  How will wading birds respond?
Developed new wading bird suitability module
  Used only hydrologic drivers for this iteration
  Determine feasibility of integrating other ecological drivers
Exploratory “proof-of-concept” set of model experiments
Compare responses between current vs modified 2-17 gauge regulation schedule

## Slide 3: ELMwca2a Application
Maps: WCA-2A basin, 500 m grid scale
  Initial land elevation: 2003 USGS HAED 400 m data
  Initial soils: Future scenarios - 2003 UF soil mapping project Historical calibration – 1991 Reddy, backward extrapolation
  Initial cattail extent: Future scenarios – 2003 Zweig Historical calibration – 1982 Rutchey
Consumer (wading bird suitability) module
  Used only hydrologic drivers for this iteration
  Calculate 2-wk recession rate
  Classify suitability of surface water depth, recession rates during bird breeding season
Boundary conditions
  Rainfall: Future scenarios - 1965-2000 SFWMM grid-IO Historical calibration – 1981-2000 SFWMM grid-IO
  TP inflow concentrations: Future scenarios – fixed 10 ppb Historical calibration – 1981-2000 DBHydro observed data

## Slide 4: ELMwca2a Application
Stage calibration
Surface water TP conc. calibration

## Slide 5: ELMwca2a Application: Consumer Module

## Slide 6: Future Scenarios: Water Management
Stage regulation methods
  Inflow sources: STA-2, S-10A-E
  Outflow sources: S-11A-C, S144-146
  Evaluate time-varying Target stage (NGVD ‘29) at WCA-2A 2-17 gauge
  Inflow when stage < (Target - Offset) {2 cm Offset}
  Outflow when stage > (Target + Offset) {2 cm Offset}
  All Inflow magnitudes assume unlimited sources (i.e., no limits of water availability, or water quality, for inflows)
  All Outflow magnitudes assume unconstrained flows allowed into receiving basins (i.e., no limits to water outflows)
  The “Bird_structOnly” run has no rainfall, ET, or groundwater inflows/outflows – thus represents the rate at which the basin can be managed to meet the stage Target w/o natural variability.

## Slide 7: Scenarios
Bird_structOnly
  No natural nor SFWMM boundary conditions (i.e., no rainfall, ET, structure, nor groundwater flows)
  Only ELM-calculated water control structure flows have inflow into/out-of the model domain
BASE2010
  All water management driven by SFWMM v6.6 2010BASE
birdSched
  ELM-calculated water control structure flows, using the proposed water management schedule for 2-17 gauge
  SFWMM v6.6 2010BASE stage boundary conditions (drives any groundwater flows)
currentSched
  ELM-calculated water control structure flows, using the current water management schedule for 2-17 gauge
  SFWMM v6.6 2010BASE stage boundary conditions (drives any groundwater flows)

## Slide 8: Scenarios

## Slide 9: Performance Measures: All

## Slide 10: Performance Measures: Bird Parameters

## Slide 11: Water Management – 2-17 Gauge (20 yr)
Simulated stage at the WCA-2A 2-17 gauge under the
-- historical calibration run (what "really" happened),
-- 2010 Base run (what "would have" happened if current ops etc. were used), and
-- current stage regulation schedule target at the 2-17 gauge

## Slide 12: Water Management – 2-17 Gauge (36yr)

## Slide 13: Water Management – 2-17 Gauge (5 of 36 yr)

## Slide 14: Basin Water Budgets, 2010BASE vs CurrentSchedule (36yr)

## Slide 15: Annual Basin Budgets, CurrentSchedule vs BirdSchedule

## Slide 16: Wading Bird Performance Measure Summary: Annual

## Slide 17: Wading Bird Performance Measure Summary: Monthly

## Slide 18: Example Bird Performance Measure: Depth Classes
CurrentSched Bird – Current BirdSched
Yellow/Brown Difference =
BirdSched higher than CurrentSched
Map header (yellow highlight) label-syntax: ScenarioName.TemporalStatistic.VariableName_DateOfOutput;
the temporal statistics are either Raw (raw output, no summary), MeanRaw (daily mean over a 30d bin), MeanPOS (mean over the 36yr Period Of Simulation), GeoMeanAnn (annual geometric mean), or for calculated rates - the rate between a beginning-date and ending-date (for P accumulation and peat accretion rates).

## Slide 19: Example Bird Performance Measure: Recession Rate Classes
CurrentSched Bird – Current BirdSched
Yellow/Brown Difference =
BirdSched higher than CurrentSched

## Slide 20: Example Other-Eco Performance Measure: P Accumulation
CurrentSched Bird – Current BirdSched
Yellow/Brown Difference =
BirdSched higher than CurrentSched

## Slide 21: P Accumulation: reflux from high initial-P soils
Upstream
Downstream
Basin-wide atmospheric
load =
25 mg/m2/yr

## Slide 22: Example Other-Eco Performance Measure: Soil P Concentration
CurrentSched Bird – Current BirdSched
Yellow/Brown Difference =
BirdSched higher than CurrentSched

## Slide 23: Example Other-Eco Performance Measure: Surface Water P Concentration
CurrentSched Bird – Current BirdSched
Yellow/Brown Difference =
BirdSched higher than CurrentSched

## Slide 24: Example Other-Eco Performance Measure: Habitat Type
CurrentSched Bird – Current BirdSched
Yellow/Brown Difference =
BirdSched higher than CurrentSched

## Slide 25: Example Other-Eco Performance Measure: Macrophyte Biomass
CurrentSched Bird – Current BirdSched
Yellow/Brown Difference =
BirdSched higher than CurrentSched

## Slide 26: Example Other-Eco Performance Measure: Peat accretion
CurrentSched Bird – Current BirdSched
Yellow/Brown Difference =
BirdSched higher than CurrentSched

## Slide 27: Wading Bird Suitability Project: General Observations
Current Schedule vs. SFWMM 2010 Base
  Base had 3X more water flows into-out-of basin than necessary for maintaining 2-17 gauge regulation stage
  Those flows associated with outflows to NE WCA-3A
Bird Schedule vs. Current Schedule
  BirdSched requires less total water
  BirdSched generally more suitable recession rates, but generally less suitable (deeper) depths
  … but those deeper depths probably more suitable to support other ecosystem dynamics…
  Both generally similar regarding phosphorus, soils, & vegetation
Future development/application
  Improve depth distributions (& wading bird suitability) by using stage targets in north & south (instead of 1 central gauge)
  Incorporate “hooks” to affect birds by vegetation density, fish indices (planning to incorporate Trexler stat model)
  Make regional evaluations of bird suitability